## Slide 1
Using Raspberry Pi to Capture Environmental Factors that Affect Sleep
Hengxin Cui
Chao Guo
Tao Tang
Yixin Wu
Lei Xu

## Slide 2: Team Members
Hengxin Cui
Yixin Wu
Chao Guo
Tao Tang
Lei Xu

## Slide 3: Idea
Star Trek Tricorder medical scanning
https://www.youtube.com/watch?v=1Mtk0BwcLoI
Fitbit

## Slide 4: SNexus
Internet of Things application/product
Sleeping data collection and analytics
    Raspberry Pi
    Sensors: sound, light and motion
    MongoDB
    Amazon Web Services EC2
    Website: http://52.26.51.149

## Slide 5: Prototype
Raspberry Pi with sound and light
Raspberry Pi with motion sensor

## Slide 6: Business analysis

## Slide 7: backgroung

## Slide 8: background

## Slide 9: Business requirement
Good sleep is essential to everybody
People always have few knowing about their sleep quality
Sleep quality is in relation with the sleep environment
Our product can collect data related to sleep and give feed backs to user.

## Slide 10: existing Products

## Slide 11: What makes us unique
More valuable data service
More Reliable Comparing with Simple Devices

## Slide 12: Demo demonstration

## Slide 13: Web application link
http://52.26.51.149/

## Slide 14: Infrastructure

## Slide 15: Infrastructure A—Aborted Infrastructure

## Slide 16: Issue and Challenge
Expenses
Programming Challenge
Amazon Kinesis Connector Library only in Java
Budget | $500
Hardware(Raspberry Pi + Sensors) | $400
AWS(Anticipated)—Kinesis + DynamoDB + EC2---6 months | $185.04 ($30.84/month)

## Slide 17: Infrastructure B

## Slide 18: HARDWARE

## Slide 19: Hardware
Raspberry Pi
  A series of credit card–sized single-board computers
  Portable, affordable ,
  Wide range of use
    Robots, Gameboy, Audio player, tablet, etc.
Notes: Hardware, it is one of the most important part since we deceived to create our own Internet of Thing project, we first need a prototype which can help us track and record the data , which is the sound volume data, light intensity data, and motion acceleration data.
And , we used Raspberry Pi to achieve it !
Raspberry Pi: Is a low cost, credit card sized computer which has built in python runtime library, so it can be programed in Python without any newly added packages. Scarcities some of the CPU and memory performance, it has the advantage of portability and affordability .
It has 4 USB and a HDMI input, which allow Raspberry Pi to connect the mouse, keyboard and monitor, and also , the most important is that Raspberry pi has multiple pins for different use, like normal IO pin, SCL, SDA pins, and so on.
Raspberry can be used widely, like making a robot, a Gameboy, even some fancy things like audio player, tablet ,etc. In our project, we connected it with sensors, to make a sleep tracker.

## Slide 20: Hardware
Peripheral equipment
  Mouse, Keyboard, Wi-Fi Dongle, Breadboard
Electronic component
  PCF8591 AD/DA Converter Module
  Analog Ambient Light Sensor
  Arduino compatible Mini Sound Sensor
  MPU 6050 3 Axis analog gyro sensors
Notes: Not only the basic peripheral equipment like keyboard, mouse, we need electronic components ,the sensors. So I am going to give a quick list of the components we use in our project. PCF8591, which used for converting the analog input to digital output. Analog Ambient Light Sensor, Arduino compatible Sound Sensor and the MPU 6050 3 Axis sensors. Because the output of these sensors are analog signal, and raspberry pi only accept digital signal, so that why we need to use the PCF8591.

## Slide 21: Technology
Analog to Digital
Notes: To finish this analog to digital conversion, so we designed the circuit like the left bottom diagram, sensors connect to the pins input 0, and input 1 , and connect the SCL and SDA pins to the same pins of Raspberry Pi. These two pins are used for I2C use, which I am not going to explain here in detail. And the diagram next to it shows the connections using breadboard, which is the gray board used for easy connection.

## Slide 22: Python
Libraries:
  SmBUS-- Allows SMBus access through the I²C interface on Linux hosts.
  Pymongo – Allows connections to MongoDB
  Request – Allows making HTTP request and get response from server
  PyTkinter – Allows to create an UI in python.
Notes: We use python for scripting the sensors and raspberry Pi, the library SmBus help us do that. The Pymongo is the library we used to interact with mongoDB, and Request is used for sending request and get response from server, and the pyTkinter, is used for making the login GUI for users.

## Slide 23: Difficulties , obstacles and solution
Linux operating system
  Why we can not connect to Wi-Fi?
  What is that error means?
Circuit design
  How to make sound and light sensors more sensitive?
Python scripting
  Which address are these value stored?
  How to retrieve the value read from pins?
Notes: We did face pretty much challenges in this hardware part, it’s much more hard than what we thought at the beginning, so that’s why it cost us more than a month on it .
Like the second one, because we had no experience using Linux system, many operations we would see some error showed, and we need to research how to fix the error, which , result in more errors during this fix process. These would slow down the process.
The third problem , finally we find that we need to add an amplifier to make the sensors more sensitive, the around 5 dollars sensors is not as accurate as what we think, and also , we need to design some complex circuit for amplification, and reduce the noise, and finally we decided not to go too much deep on it because of the time issue.
Also we still face difficulties in python programming, not like how to code in python , but more specific like how to retrieve data from sensors, but finally we concord them all, and came with our first milestone.

## Slide 24: Platform and database

## Slide 25: Platform and database
Platform: Amazon Web Services - Elastic Compute Cloud (EC2)
Database: Mongo DB
  Sensor: Store all users’ sensor data, includes lightrecord, soundrecord and motionrecord. These are the original data, which collected from raspberry pi.
  User: Store all the user information, such as login info and profiles
  Motiondatas: Store the users’ motiondata, specifically, these data are cleaned up and well analyzed.
  Sleepquality: Store the users’ sleep quality data.

## Slide 26: Server side: Node.js and Express.js
Why node.js?
  A JavaScript runtime built on Chrome's V8 JavaScript engine.
  Node.js uses an event-driven, non-blocking I/O model that makes it lightweight and efficient.
  Node.js' package ecosystem, npm, is the largest ecosystem of open source libraries in the world.
Restful api server
  A uniform interface separates clients from servers.
  Clients are not concerned with data storage, which improves portability.
  Servers are not concerned with user interface or user state, which makes server more scalable.

## Slide 27: Api structure
URL | GET | POST | PUT | DELETE
user/sensorDate | Parameters: username, sensor Response: (200) A JSON object includes a list of sensor data (204)Not found | none | none | none
user/login | Parameters: username, password Response: (200) username (401)” password is not correct” (404)” Username nor exists” |  |  | 
user/register | Parameters: username, password, email Response: (200) username (201) “Username exists!” |  |  | 

## Slide 28: Api structure
URL | GET | POST | PUT | DELETE
user/resetPassword | Parameters: username, oldPassword, newPassword Response: (200)” Password has been updated (401) "Old password is not correct” | None | None | None
user/overview | Parameters: username, sensor Response: (200)A JSON object includes the date. (404)Not date |  |  | 
user/profile | Parameters: username Response: (200)A JSON object includes user’s profile data | Parameters: username, firstname, lastname, gender, age Response: (200) 'Profile update success' |  | 

## Slide 29: Client: Backbone.js and Chart.js
User register and login
Personal profiles management
Data center overview
Data visualization and presentation
General report for user’s sleep quality

## Slide 30: UI: Bootstrap.js, jQueryUI
jQueryUI: datapicker

## Slide 31: Overview structure
Mongo DB
Server
Client
Raspberry Pi
Sensors Data
Data
Data
Ec2 instance:
mongodb://52.25.49.72:27017/capstone
DB Version: MongoDB 3.0
Ec2 instance:
http://52.26.51.149:3000/
Node.js(v4.2.3LTS) + Express.js = Restful Api server
Backbone.js + Chart.js
Bootstrap.js + jQueryUI

## Slide 32: Sleeping Data Analysis

## Slide 33: Two Questions
What’s the comparison of movements by hour during sleeping?
2. What’s the length of deep sleeping time?

## Slide 34: CAPTURE THE Data

## Slide 35: Raw Data
M =
14,000 + rows per hour
100,000 + rows per night

## Slide 36: Original or Incremental?
Step

## Slide 37: By M or By X, Y, Z ?

## Slide 38: What’s the comparison of movements by hour?

## Slide 39: Calculate the Counts of Movements By Hour
Calculate the average value and standard deviation of the dataset
b. Set the scope of normal movements
c. Count the number of outliers

## Slide 40: Differences by Hours

## Slide 41: By Hour or By night?

## Slide 42: Visualize the Movements by Hour

## Slide 43: What’s the length of deep sleeping time?

## Slide 44: CalculatION MODEL
Classified sleep into two stages: deep sleep and light sleep
Recorded the time R when roll-overs were detected
Intervals exceeding the threshold (T4 = 20 min) were classified into deep sleep
Cited From: Miwa, H.,Sasahara, S.-i., Matsui, T.
Roll-over Detection and Sleep Quality Measurement using a Wearable Sensor.
Engineering in Medicine and Biology Society, 2007. EMBS 2007.
29th Annual International Conference of the IEEE, (pp. 1507 - 1510)

## Slide 45: Calculate the Number of Movements By Hour
a. Simplify the data by each minute
b. Find out the roll-over moments and the time they happen
c. Calculate the Deep Sleep Time by looping the time intervals

## Slide 46: Accumulated Movements Value by Minute

## Slide 47: Calculate Deep Sleeping Time
Using SQL Server, loop the whole data set and finally calculate the results as:
Deep Sleeping Time: 327 Min
Deep sleep rate = 327/454 = 72%.

## Slide 48: Implementation of Past knowledge
MSIS2602 Information Systems Analysis and Design
MSIS2606 Software Project Management
MSIS696 Business of Cloud Computing
MSIS696 Web Programming

## Slide 49: New things we learnt
Hardware Installation
Python
Linux Shell Script
Node.JS
Backbone.JS
Business Intelligence

## Slide 50: Future enhancement
Hardware
Web Application
Data Analysis

## Slide 51: Thank you!